## Slide 1
Feedback and post-occupancy data on 20 near Passivhaus retrofits
Marion Baeli

## Slide 2
Content:
Retrofit for the Future and RIBA publication
RIBA Book
Monitoring results – Property 1, 2, 3, 4

## Slide 3
POST OCCUPANCY EVALUATION | PRINCEDALE ROAD
1. retrofit for the future programme
Initiative from: Small Business Research Initiative (SBRI)
With: Local Government – Homes and Community Agency
Delivered by: Technology Strategy Board

## Slide 4
Programme:
    Launched in 2009
    100 projects have been completed
    £150,000 funding per dwelling
    2 phase competition

## Slide 5
www.retrofitanalysis.org
Programme official results:

## Slide 6
Source of CO2 emissions in a standard Victorian House
80% CO2 reduction
TSB competition target
Aim:

## Slide 7
80% reduction in CO2 compared to 1990 emissions
CO2 emissions limited to 17 kg/m2.yr [20 kg/m2.yr for PHPP]
Primary Energy limited to 115 kWh/m2.yr [PassivHaus is 120kWh/m2.yr ]
Temperature
Relative Humidity
CO2 concentration
(Occupant interviews)
RftF Programme comfort monitoring:
RftF Programme main targets:

## Slide 8
CO2 concentration
~1000 – 1500ppm
Relative Humidity
~40 – 60%
Temperature:
~21oC
Comfort definition

## Slide 9
POST OCCUPANCY EVALUATION | PRINCEDALE ROAD
2. book
residential retrofits, 20 case studies

## Slide 10
Author: Marion Baeli
Co-Author: Technology Strategy Board
Publisher: RIBA
Funding & Copyright: Paul Davis + Partners
Publication

## Slide 11
Content:
- Description of each strategy
- Vital statistics
- Detailed isometric section
- Costs (material & labour)
- Monitoring data:
Energy & Internal comfort
- ID card + summary of measures
- Special feature

## Slide 12
20 project locations

## Slide 13
POST OCCUPANCY EVALUATION | PRINCEDALE ROAD
3. POE case studies

## Slide 14
Property 1 (Princedale Road)
Victorian
Mid-terrace house
5 occupants

## Slide 15
Property 1 (Princedale Road)
Fabric:
Continuous internal insulation
Triple glazing
No cold bridges (joist ends detached)
Services:
MVHR (Genvex Combi)
Solar thermal
Below ground heat exchanger
Airtightness
0.34 m3/m2h@50Pa

## Slide 16
Joist end

## Slide 17
Insulation
Foam Glass
OSB airtight layer
Underground Heat Exchanger

## Slide 21
Property 2 (The Nook)
Victorian
Detached house
6 occupants (all adults)

## Slide 22
Property 2 (The Nook)
Fabric:
IWI & EWI
Triple & Double glazing
Some cold bridges (joist ends)
Services:
MVHR (Paul)
Gas boiler
Solar thermal
Airtightness:
3 m3/m2h@50Pa

## Slide 24
Property 2 (The Nook)

## Slide 25
Property 2 (The Nook)

## Slide 26
Property 2 (The Nook)

## Slide 27
Property 3 (Passfield Drive)
1950’s
Terraced house
8 occupants (family)

## Slide 28
Property 3 (Passfield Drive)
Fabric:
EWI
Triple glazing
Minimal cold bridges (floor/wall)
Services:
MVHR (Paul)
Gas boiler
Solar thermal
Airtightness:
1.4 m3/m2h@50Pa

## Slide 29
Property 3 (Passfield Drive)
(3.5 months)

## Slide 30
Property 3 (Passfield Drive)

## Slide 31
Property 3 (Passfield Drive)

## Slide 32
Property 4 - Penzance
1950’s
Semi-detached house
2 occupants

## Slide 33
Property 4 - Penzance
Fabric:
EWI
Triple glazing
Minimal cold bridges (ground/wall)
Services:
MVHR
Ground source heat pump (Calorex 3.5 kW) & pressurised cylinder
‘Heat pod’ extension
Photovoltaic panels
Airtightness:
5.25 m3/m2h@50Pa

## Slide 34
Property 4 - Penzance

## Slide 35
Property 4 - Penzance

## Slide 36
Property 4 - Penzance

## Slide 37
POST OCCUPANCY EVALUATION | PRINCEDALE ROAD
conclusion

## Slide 38
Results CO2 emissions
26
Average post
Average pre
100

## Slide 39
Results CO2 emissions reduction
70%
Average post

## Slide 40
3 projects out of 20 met the target for Primary Energy of 115 kWh/m2.yr
Target
Primary energy demand
70%
reduction
Average post-retrofit
161
Average pre-retrofit
490

## Slide 41
Air permeability
Post
4
Pre
~11
PassivHaus

## Slide 42
Princedale
More on  ‘2012 Conference Presentations’

## Slide 43
Urgency of retrofitting the UK Housing Stock
Retrofit for the Future programme
A platform for engaging the industry into retrofits
More research needs to be undertaken on airtightness, costs,
  procurement, training, methodology…
The 20x case studies are a source of information and inspiration
for others
Results on quality of internal comfort in these retrofits are
good and encouraging

## Slide 44
Thank you
ribabookshops.com/retrofit